## Slide 1: Unit-VI

## Slide 2
WSN
Cellular M2M
Software for IoT Applications
Hardware

## Slide 3: Sensing and Sensors
Sensing is a technique used to gather information about a physical object or process, including the occurrence of events
An object performing such a sensing task is called a sensor
A sensor, then, is a type of transducer that converts energy in the physical world into electrical energy that can be passed to a computing system or controller.

## Slide 4: Sensing and Sensors
An example of the steps performed in a sensing (or data acquisition) task
Phenomena in the physical world are observed by a sensor device
The resulting electrical signals are passed through a signal conditioning stage (tasks like amplification/attenuation/noise removal)
Analog signal is transformed into a digital signal using an analog-to-digital converter (ADC)
Signal is ready for further processing/ visualization/ storage
Many wireless sensor networks also include actuators which allow them to directly control the physical world

## Slide 5: Sensing and Sensors
Data Acquisition and actuation

## Slide 6: Sensing and Sensors
Sensor types
  If the sensors require external power, they are referred to as active sensors. That is, they must emit some kind of energy (e.g., microwaves, light, sound) to trigger a response or to detect a change in the energy of the transmitted signal.
  passive sensors detect energy in the environment and derive their power from this energy input – for example, passive infrared (PIR) sensors measure infrared light radiating from objects in the proximity

## Slide 7: Sensing and Sensors
Sensor types

## Slide 8: Wireless Sensor Networks
When many sensors cooperatively monitor large physical environments, they form a wireless sensor network (WSN)
Sensor nodes communicate not only with each other but also with a base station (BS) using their wireless radios, allowing them to disseminate their sensor data to remote processing, visualization, analysis, and storage systems

## Slide 9: Wireless Sensor Networks
An example WSN with two sensor fields and their respective base stations

## Slide 10: Wireless Sensor Networks
IEEE 802.15.4 is the protocol specifically designed for low power consumption wireless networks and is supported by most of the commercial sensor nodes.
When each node is within the range of the base station, it directly communicates with the base and forms a single-hop star topology.
In case of large geographical coverage, communication is done via intermediate nodes forming multi-hop mesh topology
In multi-hop topology, nodes must be capable of propagating sensor data towards base station.

## Slide 11: Wireless Sensor Networks
Single-hop vs Multi-hop WSN

## Slide 12: Challenges & Constraints
Energy
  Contention-based MAC strategies result in higher power consumption as the nodes may try multiple times to get access of the medium and may need to listen to the medium continuously
  Therefore Contention-free MAC strategies are preferred as they allow strictly regulated medium access and allow nodes to turn off their radios when no communication is expected

## Slide 13: Challenges & Constraints
Wireless Networking
  a radio frequency (RF) signal fades
  Multi-hop networks
  Duty cycles further increases the problem

## Slide 14: Challenges & Constraints
Self Management
  Ad-hoc deployment
    Deployment in predetermined locations is always not possible. Nodes have to determine their locations, search for available communicating nodes and work
  Unattended operation
    configuration, adaptation, maintenance, and repair must be performed in an autonomous fashion without human intervention

## Slide 15: Challenges & Constraints
Decentralized Management
  Due to large scale and energy constraints topology and routing management by base station is not feasible. Nodes have to collaborate with neighboring nodes and work through a non-optimal algorithms
Design Constraints
  Cheaper
  Small in size
  Energy efficient
  Wireless connectivity
Security
  Unattended and wireless communication makes then susceptible to many security attacks i.e. Denial-of-service attacks

## Slide 16: WSN Applications
WSNs have many advantages over traditional networking techniques.
They have an ever-increasing number of applications, such as infrastructure protection and security, surveillance, health-care, environment monitoring, intelligent transportation, and smart energy

## Slide 17: WSN Applications
The applications can be divided in three categories:
  Monitoring of objects.
  Monitoring of an area.
  Monitoring of both area and objects.

## Slide 18: WSN Applications
Monitoring Area
  Environmental and Monitoring
  Precision Agriculture
  Indoor Climate Control
  Military Surveillance
  Intelligent Alarms

## Slide 19: WSN Applications
Example: Precision Agriculture
  Precision agriculture aims at making agricultural operations more efficient, while reducing environmental impact and cost.
  The information collected from sensors is used to evaluate optimum sowing density, estimate fertilizers and other inputs needs, and to more accurately predict crop yields.

## Slide 20: WSN Applications
Monitoring Objects
  Structural Monitoring
  Condition-based Maintenance
  Medical Diagnostics
  Urban terrain mapping

## Slide 21: WSN Applications
Monitoring Interactions between Objects and Space
  Wildlife Habitats (Collar mounted sensors)
  Disaster Management
  Emergency Response
  Asset Tracking
  Health Care

## Slide 22: WSN Applications
Example: Structural Health Monitoring
  Global and local inspection of structures
  Factors making WSN suitable for global inspection:
    can be placed in areas that are inaccessible
    By deploying a large number of nodes, it is possible to establish correlation between different measurements
    does not require disruption of the normal operation of the structure

## Slide 23: WSN Applications
Example: Structural Health Monitoring
  Sensing seismic events
    Challenges:
      restrictions regarding the characteristics of the excitations
      measurement noise
      environmental constraints

## Slide 24: WSN Applications
Biomedical / Medical
  Health Monitors
    Blood pressure
    Oxygen saturation
    Heart rate
  Hospital Sensors
    Monitor vital signs
    Record anomalies
    Monitor patient movements

## Slide 25: WSN Applications
Numerous industrial and commercial applications:
  Agricultural Crop Conditions
  Inventory Tracking
  In-Process Parts Tracking
  Automated Problem Reporting
  Theft Deterrent
  Plant Equipment Maintenance Monitoring

## Slide 26: WSN Applications
Example: Traffic Control
These systems gather information about the density, sizes, and speed of vehicles on roads; detect congestions; and suggest to drivers some alternative routes and emergency exits
Common methods used:
  Video
  sonar
  Radar
  Piezoelectric cables

## Slide 27: WSN Applications
Military
  Enemy tracking, battlefield surveillance
  Target detection
  Monitoring, tracking and surveillance of borders
  Nuclear, biological and chemical attack detection

## Slide 28: WSN Applications
Mobile Group Movement
  Future military: attacking by sensor nodes
  It needs coordination between nodes
  Combination between AI (artificial intelligence), sensor technology and wireless communications
  There is a goal for the nodes

## Slide 29: Cellular M2M Application Networks
Monitoring Sensing
Communication Network
Monitoring Software

## Slide 30: Software for IoT applications
Standardized End-to-end (E2E) Solution
1. Scalable Service Platform
2. Service Oriented Architecture
3. RESTful Architecture and so on.

## Slide 31: Hardware
Main Hard devices used in the M2M Network are
Sensors
Memory Processors
Actuators
RFID
ADC/DAC
Power Module
Communication Module